## Slide 1
Reinforcement Learning based Energy Optimization in Heterogeneous Wireless Sensor Networks
Department of Electronics and Communication Engineering National Institute Technology
Patna 800005
Guided By
Prof. Bharat Gupta
Electronics and Comm.
Presented By
Shubham Kumar (2448015)
Electronics and Comm.

## Slide 2
Presentation Outline
Background – context of mining and fatalities statistics
Causes of Fatalities – main culprits of mining fatalities
Literature Review – overview of existing clustering and routing protocols
Motivation & Problem Statement – challenges of energy imbalance and lack of adaptability
Overview of DEEC Protocol – difference between LEACH and DEEC & its algorithm at glance
Overview of Reinforcement Learning – basics of RL and Q-Learning in decision-making
Simulation Results – demonstration of optimal policy learning and acheive the objectives
Conclusion – key findings : Q-Learning improves adaptability and energy efficiency
Future Work – extensions with EEKA, K-mean and hyperparameter tuning

## Slide 3
Background
Mining Industry: The India’s major mining regions are Jharkhand, Odisha, Chhattisgarh, Madhya Pradesh and Karnataka[1].
Common Risks[2]:
  Gas leaks
  Explosions
  Roof collapses
  Equipment Failures
India’s mining sector[1]:
  Non Metallic mines (53 operational)
    Depth: Typically from 200 m to 600 m.
    Long: Typcally 2km to 4km.
  Metallic mines (182 operational)
    Depth: Typically from 1km to 4km.
    Long: Typcally 2km to 5km.
Data Source: DGMS [1]

## Slide 4
Chart: Mines Fatalities
| Roof collapses | Gas leaks | Explosions | Equipment Failures
Fatalities | 35 | 40 | 14 | 11
Mining Fatalities Statistics
Data Source: DGMS [1]
Over the 15 year period (2010 to 2025), total mine accidents reported is around 20,025 which leads to total deaths of 49,615[1].
Globally, the annual number of fatal mining accidents is estimated to be in range of 300 to 400[1].
Chart: Accidents Trend
| 2000 | 2001 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Accidents | 1489 | 1421 | 1334 | 1403 | 1202 | 1123 | 720 | 957 | 815 | 623 | 701 | 615 | 415 | 616 | 505 | 349 | 264 | 219 | 302 | 30 | 23 | 57 | 63 | 47


Data Source: DGMS [1]

## Slide 5
Causes of Mining Fatalities
Gas Accumulation (Methane, Carbon Monoxide, Hydrogen Sulfide): If sensors die due to low energy, gas levels go undetected, leads to explosions or suffocation which can be fatal[3].
Rock Falls / Roof Collapse:Vibration and structural stability sensors must operate continuously. If node energy depletes, blind spots occur and critical incidents happens[3][4].
High Temperature and Humidity Build-Up: Extreme underground heat can cause heat stroke, equipment malfunction and fire[4].
Communication Failures During Emergencies: Breakdown in communication prevents alerts from reaching control rooms. Most communication failures occur due to energy depleted sensor nodes or unstable routing[4].
Due to the unpredictable nature of mines, sensing systems often fail early when WSN nodes rapidly run out of energy. By improving energy efficiency, these networks can provide continuous monitoring and timely alerts, which reduces the risk of fatalities.

## Slide 6
Literature Review
Sl | Paper & Year | Optimization Technique Used | N/w Lifetime Improved | Limitations / Research gap
1 | Al-Kaseem et al. (2021) Optimized Energy-Efficient Path Planning with Multiple Mobile Sinks[5] | Ant Colony Optimization + Genetic Algorithm | 66% vs. standard LEACH | Heavy computation demand Static environment
2 | Raed et al. (2022) Efficient Energy Mechanism for Underground Mining Monitoring[6] | Enhanced LEACH + DEECP | 25% vs standard LEACH | No mobility support Static environment
3 | Salman et al. (2022) Optimization of LEACH Protocol for WSNs in Terms of Energy Efficiency and Network Lifetime[7] | Particle Swarm Optimization | 30% vs. standard LEACH | No mobility support Non heterogeneous environmnt
4 | Gamal et al. (2022) Enhancing Lifetime of WSNs Using Fuzzy Logic LEACH and Particle Swarm Optimization[8] | Fuzzy + Particle Swarm Optimization | 18% vs. standard LEACH | Increased control overhead from fuzzy inference
5 | Mohapatra et al. (2022) Mobility Induced Multi-Hop LEACH Protocol in Heterogeneous Mobile Network[9] | Modified multi-hop LEACH | 20% vs. standard LEACH | Assumes uniform mobility Non heterogeneous environmnt

## Slide 7
Literature Review
Sl | Paper & Year | Optimization Technique Used | N/w Lifetime Improved | Limitations / Research gap
6 | Botao Zhu et al. (2022)UAV Trajectory Planning in Wireless SensorNetworks by Deep Reinforcement Learning[10] | Used Deep Q-Network using neural network | Better Routing | Centralize control Computation heavy
7 | Tadele A. Abose et al. (2023) Optimized Cluster Routing Protocol With Energy-Sustainable Mechanisms for Wireless Sensor Networks[11] | Stable Election Protocol | 36% vs standard LEACH | No Multi-hopping
8 | Saikat Chandra et al. (2024) LoRa-Based IIoT Network for Underground Coal Mine Environment[12] | Used LoRa to perform P2P communication | N/A | Clustering is missing
9 | Aleem & Thumma (2025) Hybrid DEEC EEKA RL in IoT- WSNs[13] | Residual energy ratio (DEEC) EEKA constraints + RL | 17.5% vs standard LEACH | Computational overhead

## Slide 8
Motivation & Problem Statement
Motivation:
  Continuous sensing is critical in underground mines.
  Sensor nodes die early due to limited battery.
  Blind spots form, increasing accident risk.
  Energy efficient nodes ensure reliable monitoring and worker safety.
Problem Statement:
    Existing protocols such as LEACH and DEECP rely on static, heuristic-based cluster head selection and does not exploit node heterogeneity which leads to uneven energy consumption and premature node death. This reduces network lifetime and compromises continuous monitoring in underground mines.
Objective:
    Improve DEEC protocol by integrating Q-Learning (a part of reinforcement learning) for intelligent cluster head selection.
    Achieve improvement in network lifetime by reducing premature node deaths and energy imbalance.

## Slide 9
Overview of DEEC Protocol
DEEC(Distributed Energy-Efficient Clustering): It is a hierarchical routing protocol designed to maximize the lifetime of a WSN by balancing energy consumption among nodes[6].
The Core Problem It Solve: The "Energy Hole", in many protocols (like LEACH), CHs are chosen randomly, which leads nodes with low energy to become CHs and they die quickly.
Energy Aware Clustering: DEEC's key innovation is that CH selection is based on a node's remaining (residual) energy. Nodes with more energy have a higher probability of being selected as a CH.
Fig 2: LEACH vs DEEC

## Slide 10
DEEC Algorithm
Starts with a Baseline (p_opt):
    The protocol begins with a fixed percentage of nodes that should be CHs in any round (e.g., 5% of all nodes). This ensures network stability[6].
Compares Individual Energy to the Average (E_i / E_avg):
    This is the core of the protocol. It calculates a ratio by dividing a node's current energy (E_i) by the estimated average energy of the entire network (E_avg)[6].

## Slide 11
Overview of Reinforcement Learning
Definition: Reinforcement Learning (RL) is a learning paradigm where an agent learns to make decisions by interacting with an environment to maximize cumulative reward[13].
Agent Environment Interaction:
    Agent: Makes decisions by taking actions
    Environment: Responds with new states and rewards/penalty
    Goal: Find an optimal policy that maximizes expected return
Trial-and-Error Learning: Agent explores actions, observes outcomes and updates its strategy iteratively.
Fig 1: Agent learning behavior

## Slide 12
Value Functions and Bellman Equations
    State Value Function : It maps expected return under policy 𝜋, using MDP transition probabilities and reward function[14].
    Action-Value Function : It maps state-action pairs to expected return based on MDP dynamics. It allows RL to determine which action in a given state is best[14].
    Bellman Equations: Encode recursive relationship between the current value of a state and values of successor states using MDP’s transition and reward functions[13],[14].
    Use Case: Using these equations, we iteratively compute the optimal state value or optimal policy, as the Bellman equation is bound to converge.

## Slide 13
Model Free RL Q-Learning
Overview: Q-Learning enables the agent to learn the optimal action-value function that is 𝑄∗(s,a) through trial-and-error by maintaining a Q-table for all state action pairs.
Q-Learning Update Formula: This iterative formula solves the Bellman optimality equation for action values, allowing direct convergence to the optimal policy[14].
Q-Table: Stores Q(s,a) for all state-action pairs, where rows represent states and columns represent actions, holding expected rewards to guide the agent toward optimal actions[14].

## Slide 14
Process Flow Diagram
Fig 3: Process Flow Chart

## Slide 15
Simulation Results
Fig 4: Network Lifetime for 50 nodes
~9705
~10700
~3842

## Slide 16
Simulation Results
Fig 5: Network Lifetime for 50, 100 and 150 nodes

## Slide 17
Simulation Results
~140%
~13%
Fig 6: Network Throughput for 50 nodes

## Slide 18
Simulation Results
~10%
~11%
~11%
~150%
~160%
~155%
Fig 7: Network Lifetime Comparision for 50 nodes

## Slide 19
Simulation Result Summary
For Number of Nodes = 50 |  |  | 
Milestone | Baseline DEECP | Enhanced DEECP | Q-Learning DEECP
1st Node Death | 1203 | 315 | 508
50% Node Death | 2128 | 2117 | 2596
90% Node Death | 3476 | 5749 | 6711
Last Node Death | 3842 | 9705 | 10700
Throughput | 70kbit/sec | 160kbit/sec | 190kbits/sec
QL-DEECP vs Baseline DEECP
  +160% Network Lifetime
  +140% Throughput
QL-DEECP vs Enhanced DEECP (E-DEECP)
  +10% Network Lifetime
  +13% Throughput

## Slide 20
Conclusion
Enhanced DEECP (E-DEECP) introduces
  Three (3) level energy model and exploit node heterogeneity
  Distance aware CH selection
  But still relies on static thresholds that limits network adaptability
QL-DEECP integrates
  Q-Learning into CH selection
  Adaptive & dynamic decision making.
  Improves fairness in CH rotation.
Limitations of QL-DEECP (for Future Work Motivation)
  No spatial cluster optimization
  Lacks multi-hop routing
  Limited state representation (It does not capture complex features such as node density, cluster load, PDR)

## Slide 21
Future Work
Fig 8: Reinforcement Learning driven Hybrid Clustering

## Slide 22
References
[1] Online Data Source: Directorate General of Mines Safety (DGMS) - https://www.dgms.gov.in
[2] Online Data Source: https://www.assocham.org/uploads/files/Study_Indian%20Mineral%202022.pdf
[3] S. Saha, S. C. Bakshi, A. Pramanik and R. Lakshmanan, "On Underground Coal Mine Environment Monitoring with LoRa Range Extension," 2023 5th International Conference on Energy, Power and Environment: Towards Flexible Green Energy Technologies (ICEPE), Shillong, India, 2023, pp. 1-6, doi: 10.1109/ICEPE57949.2023.10201552.
[4] M. Amanzadeh, S. M. Aminossadati, M. S. Kizil, E. Sheridan and W. P. Bowen, "A microfabricated fibre optic sensor for methane gas measurement in underground coal mines," 2012 Photonics Global Conference (PGC), Singapore, 2012, pp. 1-5, doi: 10.1109/PGC.2012.6457999
[5] B. R. Al-Kaseem, Z. K. Taha, S. W. Abdulmajeedand H. S. Al-Raweshidy, “Optimized energy–efficient path planning strategy in WSN with multiple mobile sinks,” IEEE Access, vol. 9, pp. 79994–80007, Jun. 2021, doi: 10.1109/ACCESS.2021.3087086
[6] R. Alsaqour, E. S. Ali, R. A. Mokhtar, R. A. Saeed, H. Alhumyaniand M. Abdelhaq, “Efficient energy mechanism in heterogeneous WSNs for underground mining monitoring applications,” IEEE Access, vol. 10, pp. 100123–100138, Jul. 2022, doi: 10.1109/ACCESS.2022.3188654.
[7] F. M. Salman, A. A. Mohammedand A. F. Mutar, “Optimization of LEACH protocol for WSNs in terms of energy efficiency and network lifetime,” Journal of Cyber Security and Mobility, IEEE vol. 12, no. 3, pp. 275–296, May 2023, doi: 10.13052/jcsm2245-1439.1232.

## Slide 23
References
[8] M. Gamal, N. E. Mekky, H. H. Solimanand N. A. Hikal, “Enhancing the lifetime of wireless sensor networks using fuzzy logic LEACH technique-based particle swarm optimization,” IEEE Access, vol. 10, pp. 36935–36948, Mar. 2022, doi: 10.1109/ACCESS.2022.3163254.
[9] S. Mohapatra, P. K. Behera, P. K. Sahoo, S. K. Bisoy, K. L. Huiand M. Sain, “Mobility induced multi-hop LEACH protocol in heterogeneous mobile network,” IEEE Access, vol. 10, pp. 132895–132907, Dec. 2022, doi: 10.1109/ACCESS.2022.3228576.
[10] Zhu, B., Bedeer, E., Nguyen, H. H., Barton, R., & Henry, J. (2022). “UAV Trajectory Planning in Wireless Sensor Networks for Energy Consumption Minimization by Deep Reinforcement Learning”. IEEE Transactions on Vehicular Technology, 70(9), 9540–9554. doi:10.1109/TVT.2021.3102161
[11] Abose, T. A., Tekulapally, V., Kejela, D. C., Megersa, K. T., Daka, S. T., & Jember, K. A. (2024). “Optimized Cluster Routing Protocol With Energy-Sustainable Mechanisms for Wireless Sensor Networks.” IEEE Access, 12, 99661-99671. doi:10.1109/ACCESS.2024.3429645
[12] Chowdhury, A. R., Bakshi, S. C., Pramanik, A., & Roy, G. C. (2024). “Design and Study of LoRa-Based IIoT Network for Underground Coal Mine Environment.” IEEE Access. DOI: 10.1109/ACCESS.2024
[13] Abdul Aleem & Rajesh Thumma “Optimizing Energy Efficiency in IoT-Enabled Wireless Sensor Networks Using an Integrated EEKA-K-means Approach” by EEE Sensors Journal, 2025. DOI: 10.1109/JSEN.2025.3582381
[14] Available Online Book : https://web.stanford.edu/class/psych209/Readings/SuttonBartoIPRLBook2ndEd.pdf

## Slide 24
Thank You
Open to Q&A